## Slide 1: CSE460: VLSI Design
Lecture 3

## Slide 2: CMOS Logic

## Slide 3: Contents
Silicon lattice structure
p-type and n-type semiconductors, p-n junction diode
nMOS and pMOS transistors
Transistors as switches
Basic logic gate review
CMOS gate structure
Pull-up network (PUN) and pull-down network (PDN)
Series and parallel PUN & PDN networks
CMOS implementation of AOI, OAI and other logic gates

## Slide 4: Silicon Lattice
Silicon is a semiconductor
Transistors are built on a silicon substrate
Silicon is a Group IV material
  Si (16) -> 1s2 2s22p6 3s23p2
Forms crystal lattice with covalent bonds to four neighbors
Pure silicon has no free carriers and conducts poorly
How to increase its conductivity?

## Slide 5: Doped (Impure) Silicon
How to increase the conductivity of a pure semiconductor (usually Group IV materials)?
Answer: by adding impurity! (dopants)
Adding dopants increases the conductivity
Group V dopants: provides free “electron” to the pure semiconductor (Ex: Arsenic)
  Called the n-type semiconductor afterwards
Group III dopants: provides free “holes” to the pure semiconductor (Ex: Boron)
  Called the p-type semiconductor afterwards

## Slide 6: Concept Review
n-type semiconductor
  Carrier: electrons
  Net electrical charge of the material stays the same (electrically neutral)
  Difference with pure semiconductor: it has more free electrons, even after forming bonds with the neighboring atoms
  Free electrons increase conductivity
p-type semiconductor
  Carrier: holes (absence of electrons)
  Net electrical charge of the material stays the same (electrically neutral)
  Difference with pure semiconductor: it has empty electron spaces (called holes) in certain bonds with the neighbouring atoms
  Electrons from neighbouring bonds try to fill up the empty spaces by creating a flow of electrons, hence increasing the conductivity

## Slide 7: Concept Review
A junction between p-type and n-type semiconductor forms a diode.
Current flows only in one direction
p-type to n-type, n-type to p-type

## Slide 8: Electrical Voltage ⇔ Logic Conversion
VDD = Logical High (1)
GND = Logical Low (0)
VDD = 5 V, 3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, … (electrical voltage)
GND = 0 V (electrical voltage)
VDD has decreased in modern processes
  High VDD would damage modern tiny transistors
  Lower VDD saves power

## Slide 9: MOS Transistor
Four terminals: gate, source, drain, body
  gate, source, body -> conductors, SiO2 (oxide) -> insulator
  source and drain are identical, can be used interchangeably, no difference in construction
Body is tied to the source: functionally a 3 terminal device
Depending on the voltage applied to the gate terminal, source and drain are either electrically connected or disconnected

## Slide 10: nMOS Transistor
Low voltage (GND) applied to the gate: TRANSISTOR is OFF
  source and drain are disconnected (no channel between them)
  no current flows, transistor is OFF
High voltage (VDD) applied to the gate: TRANSISTOR is ON
  source and drain are connected by an n-channel, right under the gate oxide (SiO2)
  current flows from drain to source, transistor is ON
  details on the working mechanism: later in this course!

## Slide 11: pMOS Transistor
Low voltage (GND) applied to the gate: TRANSISTOR is ON
  source and drain are connected by a p-channel, right under the gate oxide (SiO2)
  current flows from source to drain (opposite direction of nMOS), transistor is ON
  details on the working mechanism: later in this course!
High voltage (VDD) applied to the gate: TRANSISTOR is OFF
  source and drain are disconnected (no channel between them)
  no current flows, transistor is OFF

## Slide 12: MOS Transistors as Switches
Electrically controlled switches
Voltage at gate controls path from source to drain

## Slide 13: Basic logic gates

## Slide 14: CMOS
CMOS can be used to build both simple and compound logic gates
Consists of 2 networks
  pMOS pull-up network
  nMOS pull-down network
pMOS & nMOS both used in the same structure -> CMOS

## Slide 15: CMOS
Depending on inputs the networks can be ON or OFF
Network ON: Network is conducting electricity
Network OFF: Network is not conducting electricity
Depending on the inputs, 4 possible combinations of the 2 networks are possible:
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Output = Z (float) | Output = 1 (High)
Pull-down ON | Output = 0 (Low) | Output = X (indeterminate)

## Slide 16: CMOS gate structure
Pull-up: OFF
Pull-down: OFF
Output is very high impedance/Z/floating/no connection
Useful when we want to detach some part of our circuit
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Output = Z (float) | Output = 1 (High)
Pull-down ON | Output = 0 (Low) | Output = X (indeterminate)

## Slide 17: CMOS gate structure
Pull-up: ON
Pull-down: OFF
Output is pulled-up to VDD
Useful when we want to output logical high (1)
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Output = Z (float) | Output = 1 (High)
Pull-down ON | Output = 0 (Low) | Output = X (indeterminate)

## Slide 18: CMOS gate structure
Pull-up: OFF
Pull-down: ON
Output is pulled-down to GND
Useful when we want to output logical low (0)
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Output = Z (float) | Output = 1 (High)
Pull-down ON | Output = 0 (Low) | Output = X (indeterminate)

## Slide 19: CMOS gate structure
Pull-up: ON
Pull-down: ON
Output is indeterminate
  somewhere between VDD and GND, we don’t know for sure
Usually a faulty condition
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Output = Z (float) | Output = 1 (High)
Pull-down ON | Output = 0 (Low) | Output = X (indeterminate)

## Slide 20: Pull-up & Pull-down Networks
Simplest pull-up network: a single pMOS
Complex pull-up network can be build from different series and parallel combinations of pMOS transistors
Simplest pull-down network: a single nMOS
Complex pull-down network can be build from different series and parallel combinations of nMOS transistors

## Slide 21: Series and Parallel Networks: Simple case
Pull-up network: a single pMOS
  High voltage at gate input: OFF
  Low voltage at gate input: ON
Pull-down network: a single nMOS
  High voltage at gate input: ON
  Low voltage at gate input: OFF
Series combination of networks
  Every network must be ON to make the whole network conducting (figure: a, b)
Parallel combination of networks
  At least one network must be ON to make the whole network conducting (figure: c, d)

## Slide 22: Series and Parallel Networks: General case 1
Pull-up network: multiple pMOS transistors
  series combination
    Low voltage at all gate inputs: ON
  parallel combination
    Low voltage at minimum one gate input: ON
Pull-down network: multiple nMOS transistors
  series combination
    High voltage at all gate inputs: ON
  parallel combination
    High voltage at minimum one gate input: ON
Series combination of such networks
  Every network must be ON to make the whole network conducting

## Slide 23: Series and Parallel Networks: General case 2
Pull-up network: multiple pMOS transistors
  series combination
    Low voltage at all gate inputs: ON
  parallel combination
    Low voltage at minimum one gate input: ON
Pull-down network: multiple nMOS transistors
  series combination
    High voltage at all gate inputs: ON
  parallel combination
    High voltage at minimum one gate input: ON
Parallel combination of such networks
  At least one network must be ON to make the whole network conducting

## Slide 24: Conduction Complement
Rule of Conduction Complements
  Pull-up network is complement of pull-down (and vice versa)
  Parallel -> series, series -> parallel
Example: CMOS NAND-2 gate
  Pull-down: 2 nMOS in series connection with inputs A & B
  Pull-up: 2 pMOS in parallel (compliment of series) connection with the same inputs A & B
Conclusion: for any CMOS logic gate, we just need to build only one network (usually the pull-down, because its easier) and the conduction complement rule will take care of the other one!

## Slide 25: Building An Inverting CMOS Logic Gate
Build the pull-down network using nMOS transistors
  series nMOS transistor networks for inputs/signals that are “AND”ed
  parallel nMOS transistors for inputs/signals that are “OR”ed
Build the pull-up network using pMOS transistors
  Using the conduction complement rule
  Parallel networks in pull-down network will be redrawn in series for pull-up network
  Series networks in pull-down network will be redrawn in parallel for pull-up network
Connect the pull-up network (PUN) and the pull-down network (PDN) in series between VDD and GND

## Slide 26: An Example: Building the Pull-down Network
series nMOS transistor networks for inputs/signals that are “AND”ed together
parallel nMOS transistors for inputs/signals that are “OR”ed together
  Example: consider the inverting function, Y = [(A+BC)D]’
  Step 1: Individual PD networks for A, B, C, D inputs (simple case)
    4 single nMOS transistors
  Step 2: PD network for BC signal
    B & C ANDed in BC: B & C PD networks will be in series
  Step 3: PD network for (A+BC) signal
    A and BC ORed (A+BC): A & BC PD networks will be in parallel
  Step 4: PD network for (A+BC)D signal
    (A+BC) and D ANDed in (A+BC)D: (A+BC) & D PD networks will be in series
  (The term “signal” is used to describe an intermediate value which are generated from inputs. Here A,B,C,D are inputs but A+BC or BC are referred to as signal)

## Slide 27: An Example: Building the Pull-down Network
Y = [(A+BC)D]’
  Step 1: Individual PD networks for A, B, C, D inputs (simple case)
    4 single nMOS transistors

## Slide 28: An Example: Building the Pull-down Network
Y = [(A+BC)D]’
  Step 2: PD network for BC signal
    B & C ANDed in BC: B & C PD networks will be in series

## Slide 29: An Example: Building the Pull-down Network
Y = [(A+BC)D]’
  Step 3: PD network for (A+BC) signal
    A and BC ORed (A+BC): A & BC PD networks will be in parallel

## Slide 30: An Example: Building the Pull-down Network
Y = [(A+BC)D]’
  Step 4: PD network for (A+BC)D signal
    (A+BC) and D ANDed in (A+BC)D: (A+BC) & D PD networks will be in series

## Slide 31: Building the Pull-up Network
Just follow the CONDUCTION COMPLEMENT rule!!
Use pMOS transistors instead of nMOS
Parallel networks in pull-down network will be redrawn in series for pull-up network
Series networks in pull-down network will be redrawn in parallel for pull-up network

## Slide 32: An Example: Building the Pull-up Network
Y = [(A+BC)D]’
  Step 1: Individual PU networks for A, B, C, D inputs (simple case)
    4 single pMOS transistors

## Slide 33: An Example: Building the Pull-up Network
Y = [(A+BC)D]’
  Step 2: PU network for BC signal
    B & C PD networks was in series
    B & C PU networks will be in parallel

## Slide 34: An Example: Building the Pull-up Network
Y = [(A+BC)D]’
  Step 3: PU network for (A+BC) signal
    A & BC PD networks was in parallel
    A & BC PU networks will be in series

## Slide 35: An Example: Building the Pull-up Network
Y = [(A+BC)D]’
  Step 4: PU network for (A+BC)D signal
    (A+BC) & D PD networks was in series
    (A+BC) & D PU networks will be in parallel

## Slide 36: An Example: Putting it all together
Y = [(A+BC)D]’
Connect the pull-up network (PUN) and the pull-down network (PDN) in series between VDD and GND
The Output of the inverting function (Y) is taken from the common node of PUN and PDN
This is the CMOS logic gate for the given inverting logic function Y

## Slide 37: Example: CMOS NAND-2, NOR-2 and Inverter Gates
NAND-2 [ Y=(AB)’ ] NOR-2 [ Y=(A+B)’ ] Inverter [ Y=A’] logic functions can also be implemented in CMOS like this (try yourself first):

## Slide 38: Implementing non-inverting logics in CMOS
The techniques described so far can only be applied to build any inverting logic function
There are multiple ways to implement non-inverting logic functions using CMOS
The easiest way is to use an additional inverter at the output of the inverting function
Example: Y = (A+BC)D can be build like this
  Build a CMOS logic gate for Y = [(A+BC)D]’
  Connect the output of the previous gate to the input of an CMOS inverter
  The output of the inverter will be Y = (A+BC)D

## Slide 39: Example: CMOS AOI22 Gate
Y = (AB+CD)’ also called the AND-OR-INVERT-2-2 or AOI22 GATE

## Slide 40: Final Example: CMOS OAI31 Gate
Y = [(A+B+C)D]’ also called the OR-AND-INVERT-3-1 or OAI31 GATE

## Slide 41: Final Example: CMOS Implementation of 2x1 MUX using
Y = S’A + SB
How many transistors required?

## Slide 42: Thank you!