## Slide 1
CSE460: VLSI Design
Lecture 15

## Slide 2: CMOS DC Characteristics

## Slide 3: Contents
CMOS Inverter DC Characteristics
Noise Margin
nMOS & pMOS Pass Transistor DC Characteristics

## Slide 4: Static CMOS Inverter
A static CMOS inverter is built using a pMOS and an nMOS
DC Transfer function or DC response: Vout vs Vin
For the CMOS inverter shown:
Vout = VDD
Vin = VDD
⇒ Vout = 0
Vin = 0 ⇒
●
In between these 2 cases, Vout depends transistor current
Vout vs Vin relationship can be found by setting Idsn = |Idsp|
Vout vs Vin relationship can also be found via graphical solutions

## Slide 5: CMOS Inverter DC Response
CMOS Inverter DC response can be determined as:
1. Divide the input into 5 different regions:
A: 0 ≤ Vin < Vtn
B: Vtn ≤ Vin < VDD/2
C: Vin = VDD/2
D: VDD/2 < Vin ≤ VDD - |Vtp|
e.
E: Vin > VDD - |Vtp|
Determine the operating regions of the devices
  Cutoff, Linear or Saturation?
Approximate Vout at A, B, C, D & E regions depending on the pMOS and nMOS operating regions

## Slide 6
CMOS Inverter DC response
Region A

## Slide 7
CMOS Inverter DC response
Region B

## Slide 8
CMOS Inverter DC response
Region C

## Slide 9
CMOS Inverter DC response
Region D

## Slide 10
CMOS Inverter DC response
Region E

## Slide 11
CMOS Inverter DC response
Complete Vout vs Vin

## Slide 12: Practical CMOS Inverter DC response
In reality, the sharp change at region C is not that sharp and has finite slope
Theoretical inverter DC response vs Practical inverter DC response
Finite slope at region C
Infinite slope at region C

## Slide 13: Supply Current
If IDD = Idsn = |Idsp| is the supply current drawn from VDD
IDD is non-zero in regions B, C & D
IDD is zero in regions A & E

## Slide 14: Power Consumption
If IDD = Idsn = |Idsp| is the current drawn from supply VDD
IDD is non-zero in regions B, C & D
IDD is zero in regions A & E
That is why we always try to work with strong signals
A strong 0 falls in the region A where IDD ≈ 0
A strong 1 falls in the region E where IDD ≈ 0
IDD ≈ 0 or low implies low power consumption!

## Slide 15: Power Consumption
If IDD = Idsn = |Idsp| is the current drawn from supply VDD
IDD is non-zero in regions B, C & D
IDD is zero in regions A & E
That is also why we try to avoid degraded signals
A degraded 0 falls in the region B/C where IDD ≠ 0
A degraded 1 falls in the region D/C where IDD ≠ 0
IDD ≠ 0 or high implies high power consumption!

## Slide 16: Beta Ratio Effects
The crossover point, where Vin = Vout is called the input threshold, Vinv
For βp = βn, the inverter threshold voltage, Vinv = VDD/2 βp / βn is called the beta ratio; r = βp / βn
r = 1 ⇒ inverter is un-skewed
r > 1 ⇒ inverter is HI-skewed
r < 1 ⇒ inverter is LO-skewed
Thus, by changing r we can shift the response!

## Slide 17: Beta Ratio Effects for a Static CMOS Inverter
Vgsp = Vin - VDD
Vdsp = Vout - VDD
Vgsn = Vin - 0 = Vin
Vdsn = Vout - 0 = Vout
Assume: V = -V
tp tn
V
gsp
Vgsn
V
dsn
(+)
(+)
(+)
Vdsp
(+)
We would like to know how Vinv changes for a CMOS inverter as we change r
For the CMOS inverter shown:
(-) (-)
(-)
(-)

## Slide 18: Beta Ratio Effects for a Static CMOS Inverter
Vgsn
V
dsn
Vgsp (+)
(+)
(+)
Vdsp
(+)
(-)
(-)
(-)
(-)
For βp ≠ βn, we can calculate the inverter threshold voltage by setting Vin = Vinv
In region C, both pMOS & nMOS are saturated
So the nMOS and pMOS currents are:
dsp p gsp
DD tp
I = β (V - V )2/2 = β (V - V - V )2/2
I
= β (V
tp p inv
2
- V ) /2 = β (V
dsn n gsn tn n inv
tn
- V )2/2
Set the currents Idsp = -Idsn
Solve for Vinv:

## Slide 19
Beta Ratio Effects
So thus for βp ≠ βn, we can calculate the inverter threshold voltage as a function of “r”, where r = βp / βn

## Slide 20: Other CMOS Gates
DC transfer characteristics of other static CMOS gates can be understood by collapsing the gates into an equivalent inverter
Series transistors can be viewed as a single transistor of greater length
If only one of several parallel transistors is ON, the other transistors can be ignored
If several parallel transistors are ON, the collection can be viewed as a single transistor of greater width

## Slide 21: Noise Margin (Noise Immunity)
Noise margin is closely related to the DC voltage characteristics
Helps determine the allowable noise voltage on the input of a gate so that the output will not be corrupted
The specification most commonly used to describe noise margin uses two parameters:
The LOW noise margin, NML
The HIGH noise margin, NMH

## Slide 22: Noise Margin
Voltage definitions:
VIH = minimum HIGH input voltage VIL = maximum LOW input voltage VOH= minimum HIGH output voltage VOL = maximum LOW output voltage NML = The LOW noise margin
NMH = The HIGH noise margin
Driver gate
Receiver gate

## Slide 23: Low Noise Margin
The LOW noise margin (NML) is the difference in maximum LOW input voltage recognized by the receiving gate and the maximum LOW output voltage produced by the driving gate
NML = VIL - VOL
Driver gate
Receiver gate

## Slide 24: High Noise Margin
The HIGH noise margin (NMH) is the difference between the minimum HIGH output voltage of the driving gate and the minimum HIGH input voltage recognized by the receiving gate
NMH = VOH - VIH
Driver gate
Receiver gate

## Slide 25: Selecting VIL, VIH, VOL & VOH
How to choose the logic levels VIL, VIH , VOL & VOH such that the noise margins NML & NMH are maximized?
Use the DC transfer characteristics!
Driver gate
Receiver gate

## Slide 26: Selecting VIL, VIH, VOL & VOH
How to choose the logic levels VIL, VIH , VOL & VOH such that the noise margins NML & NMH are maximized?
Use the DC transfer characteristics!
Logic levels are defined at the unity gain point where the slope is –1
This gives a conservative bound on the worst case static noise margin
Driver gate
Receiver gate

## Slide 27
Selecting VIL, VIH, VOL & VOH
Logic levels of typical 5 V and 3.3 V logic families
Driver gate
Receiver gate

## Slide 28: Noise Margin: Summary
NML or NMH too small: the gate may be disturbed by noise that occurs on the inputs
An unskewed gate has equal noise margins: which maximizes immunity to arbitrary noise sources
If a gate sees more noise in the high or low input state: the gate can be skewed to improve that noise margin at the expense of the other
Driver gate
Receiver gate

## Slide 29: Noise Margin: Summary
Noise sources tend to scale with the supply voltage: so noise margins are best given as a fraction of the supply voltage; for example 0.3VDD
A noise margin of 0.4 V is quite comfortable in a 1.8 V process, but marginal in a 5 V process
Driver gate
Receiver gate

## Slide 30: Pass Transistor DC Characteristics
Recall from our previous lectures that
nMOS transistors pass ‘0’s well but ‘1’s poorly
pMOS transistors pass ‘1’s well but ‘0’s poorly
We are now better prepared to define how “poorly”

## Slide 31: nMOS Pass Transistor DC Characteristics
To keep an nMOS transistor ON, we need
Vgs ≥ Vtn
⇒ Vg - Vs ≥ Vtn
⇒ Vs ≤ Vg - Vtn
⇒ Vs(max) = Vg - Vtn

## Slide 32: nMOS Pass Transistor DC Characteristics
To keep an nMOS transistor ON, we need
●
Vs(max) = Vg - Vtn
nMOS transistors passing ‘1’ (Vin = VDD; Vout = ?)
Gate is connected to VDD: Vg = VDD
Current flowing from drain to source
Vin= Vd = VDD; Vout = Vs = ?
But we know Vs(max) = Vg - Vtn ⇒ Vout(max) = VDD - Vtn
nMOS transistors attempting to pass a ‘1’ never pass above VDD - Vtn

## Slide 33: pMOS Pass Transistor DC Characteristics
To keep a pMOS transistor ON, we need
Vsg ≥ |Vtp|
⇒ Vs - Vg ≥ |Vtp|
⇒ Vs ≥ Vg + |Vtp|
⇒ Vs(min) = Vg + |Vtp|

## Slide 34: pMOS Pass Transistor DC Characteristics
To keep a pMOS transistor ON, we need
●
Vs(min) = Vg + |Vtp|
pMOS transistors passing ‘0’ (Vin = 0; Vout = ?)
Gate is connected to GND: Vg = 0
Current flowing from source to drain
Vin= Vd = 0; Vout = Vs = ?
But we know Vs(min) = Vg + |Vtp| ⇒ Vout(min) = |Vtp|
pMOS transistors attempting to pass a ‘0’ never pass lower than |Vtp|

## Slide 35: nMOS Pass Transistor DC Characteristics
Series nMOS transistors passing ‘1’ (VDD)
Vg(T1) = Vg(T2) = Vg(T3)
= VDD
If all of the transistors have gates tied to VDD
●
●
Vin(T1) = VDD; Vout(T3) = ?
Output of Transistor T1: Vout(max), T1 = Vg(T1) - Vtn(T1) = VDD - Vtn
Output of Transistor T2: Vout(max), T2 = Vg(T2) - Vtn(T2) = VDD - Vtn
Output of Transistor T3: Vout(max), T3 = Vg(T3) - Vtn(T3) = VDD - Vtn
T1 T2
T3

## Slide 36: nMOS Pass Transistor DC Characteristics
nMOS transistor driven by degraded output
If T1 transistor has gate tied to VDD
Vg(T1) = VDD; Vin = VDD; Vout = ?
Output of Transistor T1: Vout(max), T1 = Vg(T1) - Vtn(T1) = VDD - Vtn
Output of transistor T1 is now driving the gate of transistor T2
T2 transistor has gate tied to VDD - Vtn
Vg(T2) = VDD - Vtn; Vin = VDD; Vout = ?
Output of Transistor T2: Vout(max), T2 = Vg(T2) - Vtn(T2) = (VDD - Vtn) - Vtn = VDD - 2Vtn
T1
T2

## Slide 37: Pass Transistor DC Characteristics: Summary
nMOS pass transistor
Vin = GND ⇒ Vout = GND (strong 0)
Vin = VDD
⇒ Vout(max) = Vg - Vtn (degraded 1)
Vin = VDD
pMOS pass transistor
Vin = GND
Vin = VDD
⇒ Vout(min) = |Vtp| (degraded 0)
⇒ Vout = VDD (strong 1)
Vin = 0
Vout = 0
Vin = 0
Vin = VDD
Vout = VDD
Vout = |Vtp|
Vout = Vg - Vtn

## Slide 42: Pass Transistor DC Characteristics: Summary
nMOS/pMOS pass transistors sometimes produce degraded outputs
The loss is sometimes called a threshold drop
In old processes where VDD was high and Vt was a small fraction of VDD, the threshold drop was tolerable
In modern processes VDD is significantly lower and Vt is almost ⅓ of VDD, the threshold drop can produce an invalid or marginal logic at the output
To solve this problem we use CMOS transmission gates

## Slide 43: Thank You!